## Slide 1: PLC
By:tamerPLC
مشرف التقنية الكهربائية
Eng_tamersalem@hotmail.com
Eng_tamersalem2003@yahoo.com
برعاية
TKnE.CoM

## Slide 2: Agenda
What is PLC?
History of PLC
Advantages of PLC
Logic of PLC
I/O elements
برعاية
TKnE.CoM

## Slide 3: What is PLC?
A programmable controller, formally called the programmable logic controller (PLC) can be defined as a solid state device member of the computer family.
It is capable of storing instruction to implement control functions such as sequencing, timing, counting, arithmetic, data manipulation and communication to control industrial machines and processes.
برعاية
TKnE.CoM

## Slide 4: History of PLC
The design criteria for the first programmable controller were specified in 1968 by the Hydromantic division of the General Motors Corp.
70’s Communication abilities appears
80’s Standardization on communication protocols
90’s Standardizations on programming language
00’s ?
برعاية
TKnE.CoM

## Slide 5: Prior to PLCs
Contactors and relays hard-wired together
Circuit first had to be designed and drawn up
Components were specified and installed
Electrician would then wire it all together
برعاية
TKnE.CoM

## Slide 6: With PLC
PLC can perform the same task as hard-wired devices
Connections between field devices and relay contacts take place in the PLC
Installation is less extensive
Also more complex function.
برعاية
TKnE.CoM

## Slide 7: Advantages of PLCs
Faster and less costly duplication of application
Easier and faster system changes
Integrated diagnostic and override functions
Centrally available diagnostic
Immediate documentation
Smaller size
برعاية
TKnE.CoM

## Slide 8: How PLC works
Input from field devices
  Discrete, analog input
Execution of the program
  timers, counters, data manipulation
Output to the field devices
  Discrete, analog output
PLC Scan
برعاية
TKnE.CoM

## Slide 9: Discrete Input
Most common class of input interface
Discrete type input modules recognize either ON or OF Conditions.
They are totally isolated
from the CPU
24-230 Volt AC/DC
TTL level
برعاية
TKnE.CoM

## Slide 10: Analog Input
PLCs works with continuous, or analog signals as well as discrete.
Analog signals are used to represent changing values such as speed, temperature, weight, and level
Signals range from 0-10 VDC or 4-20 mA
Module converts the analog signal to digital signal. Precision of value depends on the module(8, 12 bit)
برعاية
TKnE.CoM

## Slide 11: Application Example for Analog Input
برعاية
TKnE.CoM

## Slide 12: Application Example for Analog Input
برعاية
TKnE.CoM

## Slide 13: Discrete and Analog outputs
Discrete output module works like a switch
Analog outputs converts the digital signal to the analog signal to control outside devices such as solenoid valves, servo motors, etc.
برعاية
TKnE.CoM

## Slide 14: Contact Symbols
It is true when input status is 1
It is true when input status is 0
Coils represents relays that are energized when power flows to them
Boxes represent various instructions
برعاية
TKnE.CoM

## Slide 15: Ladder Diagram
Each rung or network on a ladder represents a logical operation.
Consists of a series of inputs, timers, counters, relays, etc.
برعاية
TKnE.CoM

## Slide 16: Instructions
Standard instructions: Found in most programs including timer, counter, math, logical, increment/decrement/invert, move, and block instructions
Special Instructions are used to manipulate data. They include shift, table, find, conversion, for/next, and real-time instructions.
High-speed instructions allow for events and interrupts to occur independently of the PLC scan time.
برعاية
TKnE.CoM

## Slide 17: Example for Timer
They are used with traffic lights, for example, to control the length of time between signal changes.
برعاية
TKnE.CoM

## Slide 18: Networking
All the PLCs in the plant can be connected via LAN
Each PLC unit can be reached remotely to reprogram or for diagnostic purposes
Data collected by PLC can be transferred to any computer in the facility.
برعاية
TKnE.CoM

## Slide 19: SIEMENS S7-200 micro PLC
برعاية
TKnE.CoM

## Slide 20: Some other Connection possibilities
برعاية
TKnE.CoM

## Slide 21: Implementation Tips
Understand the desired functional description of the system
Review possible control methods and optimize the process operation
Flowchart the operation
Document everything necessary
Not : E-stop switch must be hard-wired
برعاية
TKnE.CoM

## Slide 22: References
www.plcs.com
www.sea.siemens.com
Bryan, L.E. and Bryan E.A Programmable Controllers Theory and Implementations, An Industrial Text Co. Publication., Atlanta, 1988
برعاية
TKnE.CoM

## Slide 23: اعداد مشرف قسم التقنية الكهربائية المهندس: تامر
اذا أردت المزيد والمزيد من المواضيع التقنية يمكن الدخول الى منتديات التقنية عبر هذه الروابط :
موقع التقنية : http://www.tkne.com
منتديات التقنية : http://www.tkne.com/vb
لمراسلتنا : webmaster@tkne.com